## Slide 1
New fission-product decay data measurements to improve decay heat calculations
Lydie.Giot@subatech.in2p3.fr
SUBATECH,
CNRS-IN2P3, France
In collaboration with the TAS Collaboration (IFIC-Valencia, Univ. of Surrey, Subatech)
Part of this work is also included in an IAEA coordinated paper in preparation, submission foreseen this year
Exchanges with P. Dimitriou and T. Yoshida are acknowledged

## Slide 2
Motivations on Decay Heat
Nuclear stage impacted | Time of cooling
Safety systems of cooling | 0.1s to 8 days
Unloading of assemblies from core | 5 to 25 days
Fuel transport | 1 to 10 years
Reprocessing, vitrification, storage | 4 to 3000 years
Storage | 50 to 300 000 years and more
Safety/Radiation protection
Economic interests for the complete cycle (Gen II, Gen III)
Key issue for new concepts: Gen IV, innovative reactor design, innovative fuels, most of the concepts with fast neutrons => not so many data, limited reactor operation feedback
Important design parameter for a spent fuel repository

## Slide 3
- Large time range: 10-1 to 106 years
- Complex calculation (reactor modeling + depletion): quality of the code but also of the data !
- ~ 40 000 nuclear data: s, E, Branching Ratio, l, Fission Yields, n
- Important quantity to design the size/capacity of safety systems
Summation Formula
S
DH(t) = f(t) = Ni(tc) li Ei
i
n
Ni : Number of nuclei i at the cooling time tc
Ei : Total decay energy of the nucleus i
li : Decay constant of the nucleus i
Decay Heat calculations
- Increasing will of safety authorities to ask for a precise calculation & detailed uncertainty quantification
but also identification of biases in the calculation/data to improve them ….
- Interest of industry to reduce the uncertainty for economic reasons, with keeping the same level of safety
Rigorous calculation with evaluated codes associated to experimental validation
- For Gen IV reactors, most of codes developed/benchmarked for/on LWR reactors

## Slide 4
Available decay heat measurements = Possible to get/use them 
Cooling time
0.3 s
1 day
Fission Pulses 235Uth, 239Puth, 241Puth
2 years
11 years
GE Morris/ HEDL UO2, 80 PWR/BWR assemblies
CLAB UO2, 74 PWR/BWR assemblies
27 years
Foreseen to be included in the SFCOMPO NEA database
Available in AIEA CONDERC database
- 2022 new Data@CLAB : DH of 5 assemblies PWR/BWR UO2 cooling 4-21 years
Calculations performed in a blind way with same inputs: geometry, materials, reactor operation + cooling time, DH measurements given after the calculations..
Blind benchmark exercise for spent nuclear fuel decay heat, P. Jansson et al., Nucl. Sc. & Eng., 2022
- 60 new CLAB DH measurements foreseen (EPRI Report published soon)
Available Decay Heat Measurements for U/Pu cycle
Notes: GE morris/HEDL : calorimetric measurements
GE morris BWR: 3.4->4 enrichment, burnup 15-47 MWd/kg, 2-11 years of cooling
GE morris PWR: 1.1-2.5 enrichment, burnup 27-39 MWd/kg, 3-8 years of cooling
HEDL 2.5 enrichment, 26-28 burnup, coolin 3-5 years
PWR measurements only till 8 years !!!!
Be careful, number of measurements higher than number of assmeblies (several measurements time to time for some assemblies at different cooling time)
Merci experiment @OSIRIS reactor UO2 rod, cooling time:0.02-43 days, but cea/edf properties, no external access possible so far

## Slide 5
Available Decay Heat Measurements for U/Pu cycle
Blind benchmark exercise for spent nuclear fuel decay heat, P. Jansson et al., Nucl. Sc. & Eng., 2022

## Slide 6
S
DH(t) = f(t) = Ni(tc) li Ei
i
n
Depletion calculation within a reactor model + code (e.g with SERPENT)
Bateman equations solved to get Atomic Densities Ni at the cooling time
Ei is usually divided in evaluated librairies(e.g ENDF, JEFF, JENDL) in 3 parts :
Light particles component
Electromagnetic component
Heavy particles component
dNi(t)
dt
=
S
j
( bj→i lj + f sj→i ) Nj(t)
- ( li + f si ) Ni(t)
bj→i: branching ratio
f : neutron flux
Decay Heat calculations

## Slide 7
Incomplete decay schemes: overestimate Ebeta, underestimate Egamma
- Total Decay energy (Ei) measurements
Before the 90s, conventional detection techniques: high resolution g-ray spectroscopy
Excellent resolution but efficiency which strongly decreases with increasing energy
Risk of overlooking the existence of b- feeding into the high energy nuclear levels of daughter nuclei
Decay Energy and Pandemonium effect
Bias in nuclear data bases for some key FP nuclei and all their applications (safeguards, DH, antineutrinos experiments)
J. Hardy et al., PLB 71 (2) 307, 1977
=> Known as the « Pandemonium effect »
Beta intensity feeding the level 1
REAL FEEDING
Ib
I2
I3
IT
Level 3
Level 2
Level 1
Ground state
ZAN
Z+1AN-1
Qb
Gamma intensity entering the level 1
Gamma intensity leaving the level 1
Ib = IT - Ig-in-1
Ig-in-1 = I2 + I3
IT = Ig-in-1 + Ib
APPARENT
FEEDING
IT
Level 3
Level 2
Level 1
Ground state
ZAN
Z+1AN-1
Qb
Ib
Sii = 0
Not all SIi seen by the Ge detector
Apparent beta intensity
IT = Ig-out-1 = Ib
Missing
Notes: o John Milton's Paradise Lost.

## Slide 8
II. Total Decay Energy and Pandemonium effect
Courtesy of A. Algora
Decay Energy and Pandemonium effect

## Slide 9
From TAS collaboration: contacts A. Algora & J. L. Tain @Valencia, W. Gelletly@Surrey, M. Fallot@Subatech
Most suitable technique to re-measure key nuclei: Total Absorption Spectroscopy
IFIC Valencia/Subatech/Surrey TAGS collaboration
Experiments @ Jyväskylä, Finland to high precision penning trap (Pure beams)
TAGS Arrays, Valencia
Total Absorption Gamma spectroscopy technique

## Slide 10
TAGS Measurements in decay libraries
- 1990s: 50 TAGS measurements per Greenwood et al @ IDAHO National Laboratory
Also taken into account in the release of ENDF/B-VII.1 (2011)
First inclusion of 29 nuclei in JEFF-3.1.1, M. Kellett & O. Bersillon, EPJ Web Conf 146 0209 (2017)
R. Greenwood et al., NIM A 390, 95, 1997

## Slide 11
II. Decay Heat Calculation
EEM DH (MeV/fission)
Cooling time (s)
TAGS Measurements in decay libraries
Strong impact on Electromagnetic component of Decay Heat for 239Pu thermal fission
TAGS Measurements from the TAS collaboration
Same results obtained with SERPENT + JEFF 3.1.1
105Mo, 104,105,106,107Tc
Suffered from Pandemonium
In JEFF 3.3 & ENDF/B-VII.1

## Slide 12
II. Decay Heat Calculation
Published TAGS Measurements so far …
TAS Collaboration : IFIC Valencia, Univ. of Surrey, Subatech
3 experimental campaigns (2007, 2009, 2014)
+ Experiment 09/2022 @Jyvaskyla
MTAS Collaboration : Univ. of Warsaw, ORNL, Univ of Tennessee
Experiments @ Argonne National Laboratory’s CARIBU facility
Parent nuclides identified per WPEC-25 for TAGS meas. for 235U/239Pu reactors, (NEA, T. Yoshida/ A. Nichols, 2007)
+ 91,94,95Rb, 96mY
+ 89,90Rb
: also relevant for 232Th/233U cycle
In total, 29 published nuclei
A. Algora et al., EPJ A 57, 2021

## Slide 13
II. Decay Heat Calculation
Impact of TAGS data on Decay Heat calculations
- Results presented here are part of a Review paper coordinated per IAEA (P. Dimitriou) on TAGS measurements, in completion phase
- Impact of the 28 published TAGS (wo 96mY ) nuclei on Decay Heat calculations for 15 systems were studied
Systems chosen to compare to FISPACT-II DH calc. with classical libraries (ENDF/B-VII.1, JEFF3.1.1, JENDL4-0)
M. Fleming, J. C. Sublet, 2015, CCFE-R15-28
DH experimental meas. available
in IAEA CONDERC database
Serpent used for DH with JEFF libraries + TAGS data
But also used for cross-checks on DH with ENDF (FISPACT-II/P. Dimitriou) + TAGS data
or JENDL (OYAK98/ T. Yoshida & F. Minato) + TAGS data

## Slide 14
II. Decay Heat Calculation
Impact of TAGS data on Decay Heat calculations
- For each fissioning system:
- Decay Data without the Algora 2010 TAGS data: reference library or baseline
3 sets of DH calculations combining the same FY library each time with :
- Decay Data with the 2021 TAGS published data : + TAGS 2021
- Decay Data with the Algora 2010 TAGS data : + TAGS 2010
+ TAGS 2010 : improved agreement for 239Puth, 241Puth & 238Ufast
small impact for 232Thfast & 233Ufast
Same conclusions with ENDF library
239Puth
239Puth

## Slide 15
II. Decay Heat Calculation
Impact of TAGS data on Decay Heat calculations
- For each fissioning system:
- Decay Data without the Algora 2010 TAGS data: reference library or baseline
3 sets of DH calculations combining the same FY library each time with :
+ TAGS 2010 : improved agreement for 239Puth, 241Puth & 238Ufast
- Decay Data with the 2021 TAGS published data : + TAGS 2021
- Decay Data with the Algora 2010 TAGS data : + TAGS 2010
small impact for 232Thfast & 233Ufast
Same conclusions with ENDF library
241Puth
241Puth

## Slide 16
II. Decay Heat Calculation
Impact of TAGS data on Decay Heat calculations
- For each fissioning system:
- Decay Data without the Algora 2010 TAGS data: reference library or baseline
3 sets of DH calculations combining the same FY library each time with :
- Decay Data with the 2021 TAGS published data : + TAGS 2021
- Decay Data with the Algora 2010 TAGS data : + TAGS 2010
+ TAGS 2010 : improved agreement for 239Puth, 241Puth & 238Ufast
small impact for 232Thfast & 233Ufast
Same conclusions with ENDF library
238Ufast
238Ufast

## Slide 17
II. Decay Heat Calculation
Impact of TAGS data on Decay Heat calculations
+ TAGS 2010 : no impact on ELP component
235Uth
+ TAGS 2021 : ELP slightly improved in 10-400s but underestimation in 400-1000s
Hard to say on EEM wrt differences between the 3 experimental sets !
Same conclusions with ENDF library
Need of new DH fission pulse experiments 
235Uth
235Uth

## Slide 18
II. Decay Heat Calculation
Impact of TAGS data on Decay Heat calculations
+ TAGS 2021 : improved agreement of EEM component for 233Ufast, 238Ufast, 232Thfast, for cooling time below 100s
232Thfast
233Ufast
Need to investigate key FPs for cooling range > 100s
But also need of new DH fission pulse experiments 

## Slide 19
II. Decay Heat Calculation
Impact of TAGS data on Decay Heat calculations
+ TAGS 2021 : small under estimation of ELP component for 235Uth, 239Puth, 241Puth, 233Ufast & 238Ufast at cooling times ranging from 30s to 1000s
241Puth
233Ufast
Same conclusions with ENDF library
=> Only one set of experimental data, till in the errors bars for 241Puth
=> Needs for extra experimental data but also extra investigation on key FP suffering of Pandemonium effect
=> Also on going work to take into account FY and DD uncertainties through MC sampling

## Slide 20
II. Decay Heat Calculation
Impact of TAGS data on DH calculations
Impact of Fission Yields ?
239Puth
239Puth
Overestimation of EEM component for JENDL5 for 239Puth

## Slide 21
II. Decay Heat Calculation
Final remarks and Outlooks
- Further extensive assessments need to accomodate the impact of delayed neutrons on decay heat up 10s cooling time
- Further investigations are needed to improve DH exp data vs calculations :
- New Decay Heat fission pulse experiments …
- New TAGS measurements based on WPEC-25 list and IAEA consultants’ meetings
priority 1 nuclei : 99,100Zr, 98,99Nb,130m, 132Sb,138Cs, 143La
priority 2 nuclei :
84As, 85Se, 84,89Br, 91Kr, 92-95Sr, 97Y, 105Nb, 104,107Mo, 108Tc, 133Sb,
136,137Te, 139, 141, 143, 144Ba, 144-147La, 146Pr, 139-141Cs, 136,136mI, 140Xe
- Extra investigations to identify key FP & Pandemonium candidates
-- on pulse calculations
taking also into account uncertainties on Decay Data
on-going PhD @Subatech Y. Molla, 2021-2024
-- on new fuels/ reactor concepts
ex: new PhD @Subatech&LPSC M. Tazreiter 2022-2025
on Molten Salt Reactors

## Slide 22
Thank you