## Slide 1: Pulsed-Neutron Die-Away Experiments at LNNL
Daniel Siefman, D. Heinrichs, J. Holmes, M. Zerkle, C. Percher
Nuclear Criticality Safety Division
siefman1@llnl.gov
Technical Meeting on the Compilation of Nuclear Data Experiments for Radiation Characterization
IAEA
Vienna, Austria
October 10-14, 2022

## Slide 2: Pulsed Neutron Die Away Experiments
neutrons
D-T Neutron Generator
Target Material
Borated HDPE & Cd Box for well defined geometry and to reduce room return
He-3 Detector
Inject Pulse of Neutrons
Neutrons thermalize
Neutrons spatially equilibrate
Measure exponential decay in fundamental mode
Notes: Each curve shows an increasing or flat neutron population until the pulse ends at ~0.6 ms. At that point without a source, the neutrons are only leaking from the system and their population has different spatial modes. After another 50-100 μs (depending on the target material and size), the flux thermalizes, and the flux shape equilibrates.

## Slide 3: Why PNDA for TSL Validation?
Does not require fissile material
  Non-nuclear facilities, reduced costs, fewer regulations, safer
Very simple target shapes and compositions
  Reduced uncertainties in benchmarks
  Reduced material costs
  Easy to change temperature
Only sensitive to absorption and scattering of target medium
  Reduces uncertainties from other nuclear data and compensating effects
  Tune target size to vary effect of absorption vs. scattering
Well conducted experiments have uncertainties of 0.1% - 0.5%
Figure: Measurement of Lucite target

## Slide 4: Integral Parameter: α eigenvalue
Figure: Example of pulsed-die-away curve modeled in MCNP
α: flux decay-time eigenvalue [s-1]
D0 [cm2s-1] is the asymptotic diffusion coefficient
C: “cooling coefficient” [cm4s-1]
B02: geometric Buckling [cm-2]
v thermal neutron velocity (2.2 x 105 cm/s)
Σa macroscopic absorption cross section [cm-1]
Notes: The cooling coefficient captures a geometric effect where more high-energy neutrons leak at the system boundaries, which causes the average neutron population to be at a temperature lower than thermodynamic equilibrium. C is often very small relative to the absorption and diffusion terms and has a small impact on α. The exception to this is when the geometric Buckling is very large, and the B04 term becomes very important. In most cases, α is a nearly linear function of B02 with the slope of the function depending on the material cross sections.

## Slide 5: Sensitivity Depends on Target Size
Small targets (large Bucklings) are more sensitive to scattering
Large targets (small Bucklings) are more sensitive to absorption
Figure: Buckling vs. cylinder dimensions
Figure: α vs. cylinder dimensions
Scattering
Absorption
Notes: For each target, B02 can be changed by altering a certain geometric dimension, which would be done to manipulate how α is affected by different physics of the system. For instance, when the target sample is large and B02 is small, α depends mostly on absorption (Σa), i.e. not on TSLs. When the target sample is small, B02 is large and α depends primarily on D0, which itself is highly influenced by the physics of thermal scattering. Fundamentally, the sensitivity of α to thermal scattering increases with B02, or increases as the target sample size decreases.
Using one very large sample allows to nail down the absorption term in the equation , or the y-intercept in the alpha vs. buckling curve. This then allows you to verify if the base library in MCNP is performing properly (excluding TSLs). If it is not, then you can perform a correction on all the alpha values .
For each target, B02 can be changed by altering a certain geometric dimension, which would be done to manipulate how α is affected by different physics of the system. For instance, when the target sample is large and B02 is small, α depends mostly on absorption (Σa), i.e. not on TSLs. When the target sample is small, B02 is large and α depends primarily on D0, which itself is highly influenced by the physics of thermal scattering. Fundamentally, the sensitivity of α to thermal scattering increases with B02, or increases as the target sample size decreases.
Using one very large sample allows to nail down the absorption term in the equation 𝛼=𝑣Σ_𝑎+𝐵_0^2 𝐷_0 (1−𝐶𝐵_0^2 ), or the y-intercept in the alpha vs. buckling curve. This then allows you to verify if the base library in MCNP is performing properly (excluding TSLs). If it is not, then you can perform a correction on all the alpha values .

## Slide 6: Decay to Fundamental Mode Large Cylindrical Sample
Spatial Modes (l,m,n)
r
z
Focusing only on modes of Bessel function:
Fundamental Mode
Notes: Here have 8cm radius, 18 cm height cylinder. L is the integer order of the Bessel function, m is the number of zeros of the Bessel function. N is repeating modes of sin/cos functions. The fundamental mode is that which each index has its lowest value (l=0, m=1, n=1).
In practice there isn’t enough time to let all the modes decay, the statistics will get too poor. The lower order modes can be particularly troublesome.
Gray modes are those that cancel out by placing the detector at the R=0. Also by putting it at R=0, will converge quicker (Blue line is the black line), By placing at H/2, all even modes of n are eliminated by symmetry concerns because sin(n*pi/H * H/2) =0

## Slide 7: Decay to Fundamental Mode Large Cylindrical Sample
Spatial Modes (l,m,n)
r
z
Notes: Here have 8cm radius, 18 cm height cylinder. L is the integer order of the Bessel function, m is the number of zeros of the Bessel function. N is repeating modes of sin/cos functions. The fundamental mode is that which each index has its lowest value (l=0, m=1, n=1).
In practice there isn’t enough time to let all the modes decay, the statistics will get too poor. The lower order modes can be particularly troublesome.
Gray modes are those that cancel out by placing the detector at the R=0. Also by putting it at R=0, will converge quicker (Blue line is the black line), By placing at H/2, all even modes of n are eliminated by symmetry concerns because sin(n*pi/H * H/2) =0

## Slide 8: First Tests with H2O samples
Height (cm) | Radius (cm) | Buckling (cm-2)
2.28 | 2.54 | 1.90
2.79 | 3.18 | 1.34
3.05 | 3.81 | 1.09
3.52 | 4.47 | 0.836
3.79 | 5.08 | 0.712
4.63 | 6.67 | 0.480
5.98 | 7.46 | 0.324
8.32 | 10.00 | 0.178
10.19 | 12.70 | 0.119
12.97 | 15.24 | 0.0775
Table: Geometry of Water Targets
Simulations of historical experiments showed good performance of H2O
Replicated good performance provides confidence in experimental setup
Test with 10 H2O targets in Al cans
Weigh water, calculate water height with assumed density
All measured with 30-minute exposures, variable generator frequency

## Slide 9: H2O Die-Away Curves
MCNP6.2

## Slide 10: H2O Validation & Comparison to Literature
 | (cm2-s-1) | D0 (cm2-s-1) | C (cm4-s-1)
LLNL Experiment | 4.99 ± 0.49 | 34.24 ± 1.36 | 5.03 ± 0.71
LLNL Calculation | 4.25 ± 0.34 | 36.84 ± 0.94 | 2.25 ± 0.49
Bracci & Coceva | 4.87 ± 0.33 | 35.50 ± 1.49 | 4.23 ± 1.64
Nassar & Murphy | 4.68 ± 0.15 | 39.10 ± 1.31 | 5.43 ± 1.94
 |  | D0 (cm2-s-1) | C (cm4-s-1)
LLNL Experiment | 4.99 ± 0.49 | 34.24 ± 1.36 | 5.03 ± 0.71
LLNL Calculation | 4.25 ± 0.34 | 36.84 ± 0.94 | 2.25 ± 0.49
Bracci & Coceva | 4.87 ± 0.33 | 35.50 ± 1.49 | 4.23 ± 1.64
Nassar & Murphy | 4.68 ± 0.15 | 39.10 ± 1.31 | 5.43 ± 1.94
LLNL E

## Slide 11: Sensitivity to TSLs
Figure: α vs. Buckling curve for experimental and simulated data
Figure: Bias of simulations without TSLs, with ENDF/B-VII.1, and with ENDF/B-VIII.0 TSLs
Example: Historical water experiment in cylindrical geometry
  A. Bracci & C. Coceva, “The diffusion parameters of thermal neutrons in water.” Il Nuovo Cimento, 4 (1956)
Leakage
Absorption

## Slide 12: Experimental Parameters
P383 D-T neutron generator
  Maximum yield of 5 x 108 neutrons/s
  Minimum frequency of 150 Hz
  Minimum pulse width of 10 μs
Four He-3 tubes
  Operated at 1100 V
  50 ns pulse width
Time-tagging electronics
  Provides time stamps of detected neutrons, generator pulse
  ALMM, CAEN shift register (10 ns resolution)
Box to limit room return
  Borated high-density polyethylene
  Cadmium lining
Figure: AutoCAD rendering of PNDA

## Slide 13: HDPE Die-Away Curves
Figure: HDPE cylinders used in PNDA experiment

## Slide 14: First HDPE Validation
General trend of increasing bias with smaller sampler size (larger buckling)

## Slide 15: Lucite Results Polymethyl Methacrylate
Drozdowicz, Krzysztof, et al. "Thermal neutron diffusion parameters for plexiglass." Nuclear Instruments and Methods 178.2-3 (1980): 513-516.
Krynicka, Ewa, et al. Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms 251.1 (2006): 19-26.

## Slide 16: Planned Experiments & Timeline
2022/2023:
  Benchmark evaluation
  Measurements with other moderators
Benchmark uncertainty quantification especially missing mass spectrometry
October 2023: Benchmark submission to ICSBEP
2023 moderators:
  Light water, heavy water, motor oil
2024 moderators:
  Beryllium, other plastics
Figure: Measurement with HDPE.

## Slide 17: Questions, Comments, Discussion
References:
  G. von Dardel and N. G. Sjostrand, "Diffusion Parameters of Thermal Neutrons in Water," Physical Review, vol. 96, no. 5, pp. 1245-1249, 1954.
  J. Holmes, M. Zerkle and D. Heinrichs, "Benchmarking a first-principles thermal neutron scattering law for water ice with a diffusion experiment," EPJ Web of Conferences, vol. 146, p. 13004, 2017.
  J. Holmes, M. Zerkle and A. Hawari, "Validation of Thermal Scattering Laws for Light Water at Elevated Temperatures with Diffusion Experiments," in PHYSOR 2020: Transition to a Scalable Nuclear Future, Cambridge, United Kingdom, 2020.
  D. Siefman, E. Heckmaier, W. Zwyiec, D. Heinrichs, “IER-501 CED-1: Preliminary Design of a New Pulsed-Neutron Die-­Away Experimental Testbed for Thermal Scattering Law Benchmarks (PNDA),” Lawrence Livermore National Laboratory, LLNL-TR-820718, 2021

## Slide 18
Disclaimer
This document was prepared as an account of work sponsored by an agency of the United States government. Neither the United States government nor Lawrence Livermore National Security, LLC, nor any of their employees makes any warranty, expressed or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States government or Lawrence Livermore National Security, LLC. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States government or Lawrence Livermore National Security, LLC, and shall not be used for advertising or product endorsement purposes.

## Slide 19: Interpretation of Results
Need to select data to include in the fit
Too early data:
  Flux is not fully thermalized or in fundamental spatial mode
Too late data:
  Noisy (room return) and larger uncertainty in α
Chart: 
| 0 | 0.11 | 0.22 | 0.33 | 0.44 | 0.55000000000000004 | 0.66 | 0.77 | 0.88 | 0.99 | 1.1000000000000001 | 1.2100000000000002 | 1.3200000000000003 | 1.4300000000000004 | 1.5400000000000005 | 1.6500000000000006 | 1.7600000000000007 | 1.8700000000000008 | 1.9800000000000009 | 2.0900000000000007
 | 1 | 0.80252 | 0.64404 | 0.51685 | 0.41478 | 0.33287 | 0.26714 | 0.21438 | 0.17204 | 0.13807 | 0.1108 | 0.088922 | 0.071361 | 0.057269 | 0.045959 | 0.036883 | 0.029599 | 0.023754 | 0.019063 | 0.015299
Fixed Delay Time
0
t
N
Analyzed Time Interval
Variable Delay Time
Figure: Position of the analyzed time interval
Too early
Too late

## Slide 20: Fit Convergence
Figure: Convergence of integral parameter over fit intervals
Fitted α plateaus when using data interval in fundamental mode.
  Too early data lead to overestimation
  Too late data lead to underestimation
Error propagation from fit and from population statistics in plateau

## Slide 21: Effect of Shielding Box Measurements in Low-Scatter Facility
Room Return

## Slide 22: Small Targets vs. Statistics
Figure: Statistical effects on die away curves with varying target sizes
Small targets desirable for sensitivity to TSLs
They quickly leak neutrons, leading to poor detector statistics and poor fit of exponential decay
Room Return
Notes: Small targets have neutrons leak away more quickly, leading to noisier curves. The noisier curves are harder to fit and exponential to, creating more uncertainty in the data. Can observe the rate of decay, alpha, is smaller for bigger samples (dark blue).

## Slide 23: Biases
Radius (cm) | Mean C (ms-1) | E (ms-1) | (C-E)/E (%)
2.45 | 32.78 | 34.5 | -5.08
2.58 | 30.65 | 33.2 | -7.59
2.77 | 27.84 | 30.2 | -7.90
3.01 | 25.05 | 26.4 | -5.26
3.22 | 22.95 | 23.4 | -2.09
3.54 | 20.39 | 20.9 | -2.24
3.95 | 17.99 | 18.3 | -1.58
4.68 | 15.08 | 14.4 | 4.46
5.92 | 12.03 | 11.4 | 5.86
6.32 | 11.29 | 10.9 | 3.14
6.75 | 10.70 | 10.3 | 3.40
7.63 | 9.72 | 9.4 | 3.50
9.69 | 7.59 | 8.3 | -8.62
Table: Experimental and calculated integral parameters.
Figure: Calculated pulsed neutron die away curves.
Chart: Radius (cm)
| 2.4500000000000002 | 2.58 | 2.77 | 3.01 | 3.22 | 3.54 | 3.95 | 4.68 | 5.92 | 6.32 | 6.75 | 7.63 | 9.69
 | 3.15 | 2.72 | 2.66 | 2.71 | 2.59 | 2.35 | 2.42 | 2.06 | 1.73 | 1.87 | 1.85 | 1.56 | 1.32

## Slide 24: Importance of background
Measurements outside of borated HDPE box with Cd lining
After about ~1 ms, we see dominant background.
The time dependent background makes rough sense with thermal neutrons returning from the walls or floor as it starts at around ~1 ms.
If the neutrons’ velocity is 2200 m/s, and the walls are roughly 1-2 m away, we should be measuring them returning after ~1 ms.

## Slide 25: Approaches to Improve Statistics For Cylindrical Geometry
Maximize difference between fundamental and higher order modes
Detector location
  All modes except J0 have 0-amplitude at r = 0
Source orientation
  For cylinders, neutrons strike at H/2
  Eliminates even ordered modes of sin(nzπ/H)
  Maximizes flux along vertical axis
Target dimensions
  H/D = 0.894
  Balances (0,2,1) and (0,1,3)
Repeat measurements
  Pulse neutrons, allow for decay, repeat pulse
  Target size determines time for decay
Figure: Even and odd modes of sin(nzπ/H)
Notes: By placing the source on the central plane, i.e . , at z = H/2, all modes are eliminated which have a node at H/2 since symmetry requires an equal number of neutron above and below this plane. That i s , all modes for which sin(nHπ/H2) are eliminated by symmetry. sin(nπ/2)for n = 2,4,6, e t c .

## Slide 26: Effect of Target Size on Fit Different Sized H2O Cylinders
Figure: Example varying time intervals
Figure: Effect of varying time intervals on analyzed α
Notes: Presents the challenge of selecting the data to include in the fit for two different cylinders from the previous analysis: at radii of 2.405 cm and 9.690 cm. The α values were calculated for every possible combination of start and end times from when the pulse ended to the end of the MCNP tally. At certain combinations of start and end times, the non-linear least-squares fitting algorithm did not converge and an α value could not be estimated. These occurrences are shown as white regions and happen when the start and end times are too close together and not enough data is included in the fit. Too early start times can also be seen in as yellow regions where the α values are over-estimated.
How noise affects the estimated α is apparent when comparing the estimated α values from a cylinder with a radius of 2.405 cm. The α values were extremely sensitive to the data that were selected, and very large fluctuations appeared. For that same target with better statistics (the tally on the cylinder surface) the α values had much better more stable behavior and more confident results could be found no matter the bounds of data used in the fit. The larger target with a radius of 9.690 cm had much less noise than the smaller target when the detector tally was used. This allowed for more consistent α values to be estimated across the possible data ranges used in the fit. The practical implication of this result is that while small targets may be ideal for having a large sensitivity to TSLs, at too small sizes the measured counts may have too much noise for the experimental analysis to be of high-quality.

## Slide 27: Detector placement vs. harmonics

## Slide 28: Algorithm
time
period
Neutron counts and generator trigger recorded as list mode data
Few counts per pulse, but many pulses allows to reconstruct die away curve
Trigger is initiating event, ttrigger
Sum counts in bins on die away curve as ttag – ttrigger in histogram
Pulse Trigger
counts

## Slide 29: Algorithm: Sum pulse counts to construct curve
+
+