## Slide 1: A new V&V philosophy for fusion nuclear data libraries
11/10/2022
D. Laghi1,2, M. Fabbri3
1NIER Ingegneria, Castel Maggiore, Italy
2University of Bologna, Bologna, Italy
3Fusion For Energy, Barcelona, Spain

## Slide 3: Index
JADE
Nuclear data libraries and their V&V
What is JADE?
The Sphere Leakage benchmark
JADE architecture and development
Looking ahead
Our wish list
Machine Learning
Summary

## Slide 4: JADE

## Slide 5: Nuclear data libraries and their V&V
It is a complex procedure that require extensive Verification and Validation (V&V)
The nuclear data libraries production chain

## Slide 6: Nuclear data libraries and their V&V
103 isotopes in a single library
1 .ACE file per isotope
102 reactions per .ACE file (MT numbers)
~ 105 different cross sections to be verified!
Heavy automation is a necessity, which, at the same time, is an opportunity for standardization
The need for automation and standardization

## Slide 7: Nuclear data libraries and their V&V
Vs
Energy range
Different materials and cross sections
EUROFER 97
Fission rate
Fusion rate
Tritium production
Heating on superconductive magnets
Fission products
Activation issues
The fission bias

## Slide 8: Nuclear data libraries and their V&V
Vs
Keff
Nubar
βeff
Integral parameters representative of the entire system that simplifies the V&V process
complex geometries that need to be fully modelled
different regions with different needs
a detailed spatial distribution of tallies is needed
Vast amount of tallies and energy/spatial discretization
The fission bias

## Slide 9: What is JADE?
JADE is a python based software that aims to establish itself as a corner stone for a complete and extensive automated and standardized V&V procedure for nuclear data libraries, with a special focus towards fusion applications.
EFFORT FRAGMENTATION
LACK OF AUTOMATION
FISSION BIAS
LACK OF STANDARDIZATION
ISSUES
JADE

## Slide 10: What is JADE?
Waterfall approach
Implemented by means of a stage approach and > 1.5 ppy of total effort
The organization of the project

## Slide 11: What is JADE?
MCNP as transport code
Vast amount of benchmark to be automatically generated and run
Vast amount of outputs
Meaningful automatic post-processing
JADE needs

## Slide 12: What is JADE?
Benchmarks suite
COMPUTATIONAL
EXPERIMENTAL
TRANSPORT
ACTIVATION
Sphere Leakage
ITER 1D
C-model
HCPB TBM
WCLL TBM
SPHERE SDDR
ITER CYL SDDR
OKTAVIAN
FNG SDDR

## Slide 13: What is JADE
Benchmarks suite

## Slide 14: The Sphere Leakage benchmark
Benchmark description
A uniform 0-14 MeV neutron point source is inserted at the center of a sphere composed entirely by a single isotope or a typical ITER material.
All isotopes provided by the nuclear data library under assessment are singularly tested.
Tallied quantities:
Neutron and photon leakage flux (energy binned);
Neutron and photon heating inside the sphere;
Tritium and Helium production inside the sphere;
DPA.

## Slide 15: The Sphere Leakage benchmark
Excel formatted tables

## Slide 16: The Sphere Leakage benchmark
Plot atlas

## Slide 17: JADE architecture and development
General scheme

## Slide 18: JADE Architecture and development
ReadTheDocs: https://jade-a-nuclear-data-libraries-vv-tool.readthedocs.io/en/latest/
CoNDERC: https://nds.iaea.org/conderc/
GitHub: https://github.com/dodu94/JADE
Open source

## Slide 19: JADE architecture and development
Automatic testing with pytest and coverage
Help the stability of the code
Increase trust on JADE results
Sets a minimum quality standard for future contributors to the code
Speed up introduction of new features (faster verification)

## Slide 20: JADE architecture and development
Continuous Integration (CI)
At each push on the main JADE branch:
JADE is installed in a cloud Windows environment and the automatic testing is run (handled by GitHub)
The documentation is rebuilt by ReadTheDocs and adjourned

## Slide 21: JADE in numbers
12k
2
>106
9
Lines of code
Published papers
Implemented benchmarks
CPU simulation hours worth of data that has been post-processed
D. Laghi et al, 2020, “JADE, a new software tool for nuclear fusion data libraries Verification & Validation”, Fusion Engineering and Design, 161 112075. DOI: https://doi.org/10.1016/j.fusengdes.2020.112075
D. Laghi et al, “Application of JADE V&V capabilities to the new FENDL v3.2 Beta release”, Nuclear Fusion, 61 11.DOI: http://iopscience.iop.org/article/10.1088/1741-4326/ac121a

## Slide 22: Looking ahead

## Slide 23: Next foreseeable steps
CoNDERC &
Expansion of the benchmarks suite
SINBAD

## Slide 24: Machine learning: a possible mid-term future
Monte Carlo codes like OpenMC are currently porting their code to GPU solvers
Simulation time could decrease by a few order of magnitudes!
Leveraging the open source automation of benchmarks running and definition of acceptance test, ML algorithm could be introduced to support the libraries evaluation process
An example of application is NucML1: https://pedrojrv.github.io/nucml/index.html
1Pedro Jr. Vicente-Valdez, Massimiliano Fratoni (UC Berkely, USA)

## Slide 25: What it will be great to have
A comprehensive, unified, user-friendly, open-source, ready to be used database of experiment (e.g., Conderc+SINBAD GitHub).
A platform to provide feedback and record exchanges (e.g., GitHub).
A collection of computational benchmark to use (e.g., 1D ITER).
A standardized way to share and collect the different executed benchmarks in a common database (e.g., CONDERC) trying to avoid duplication.
A closer collaboration with the different parties with periodic exchange (i.e., CCFE).
Guidelines for the V&V of (fusion) libraries with clear acceptance criteria (e.g., C/E TBR : [0.95, 1.05]).

## Slide 26: Summary
JADE improves the standardization and the automation level in the field of nuclear data V&V (especially regarding fusion application).
JADE is a consolidated open-source tool built for the community by the community. If you are interested on collaborating do not hesitate to contact us. Let’s join forces.
V&V on many libraries has been already performed by JADE(i.e., FENDL3.1d, FENDL3.2, JEFF-3.3., JEFF-4.0T1). Few inconsistencies and discrepancies were spotted and reported. More work is planned.
We sincerely appreciate the effort put in place by NEA, IAEA, SINBAD to modernize the experimental database and the collaboration with the different parties to continue the development of JADE.

## Slide 27
GitHub: https://github.com/dodu94/JADE
READ THE DOCS: https://readthedocs.org/

## Slide 29: Backup slides

## Slide 30: JADE application to production cases
Proof of concept
Tested libraries:
FENDL v2.1
FENDL v3.0
FENDL v3.1d
ENDF VII.1
Known errors in the FENDL v3.1d were re-spotted by JADE consistency checks
Paper:
D. Laghi, M. Fabbri, L. Isolan, R. Pampin, M. Sumini, A. Portone and A. Trkov, 2020, “JADE, a new software tool for nuclear fusion data libraries Verification & Validation”, Fusion Engineering and Design, 161 112075. DOI: https://doi.org/10.1016/j.fusengdes.2020.112075

## Slide 31: JADE application to production cases
Proof of concept
Some examples where the leakage neutron flux results differed significantly among the tested libraries.

## Slide 32: JADE application to production cases
FENDL v3.2 release (BETA)
Important differences in key neutron related quantities were spotted for typical ITER materials when comparing the old and new release of FENDL libraries
Paper:
D. Laghi, M. Fabbri, L. Isolan, M. Sumini, G. Schnabel and A. Trkov, 2021, “Application of JADE V&V capabilities to the new FENDL v3.2 Beta release”, Nuclear Fusion, 61 11.DOI: http://iopscience.iop.org/article/10.1088/1741-4326/ac121a

## Slide 33: JADE application to production cases
FENDL v3.2 release (BETA)
Effect of the higher neutron heating in the steel layers of the ITER 1D model
B-10 accounts only for 0.00036 % (in mass) of SS316L(N)-IG and at the same time SS316L(N)-IG is composed by 45 different isotopes. Without systematic and automated testing it would have been more difficult to track the origin of the issue.

## Slide 34: JADE application to production cases
FENDL v3.2 official release

## Slide 35: JADE application to production cases
FENDL v3.2 official release (Water/O-16)
Difference in neutron heating are clearly visible in water both in ITER1D and HCPB TBM benchmarks.
IAEA nuclear data section is considering for the O-16 cross section to either to:
Switch to ENDFVIII.0 evaluation;
Correct NJOY processing routine for KERMA data