## Slide 1: Determination of stopping power for α-particles in carbon by resonance scattering
T.L. Bobrovskiy, P.S. Prusachenko, A.F. Gurbich, M.V. Bokhovko
Institute for Physics and Power Engineering, Obninsk, Russia
timofeybobrovskiy@gmail.com
IAEA Thechnical Meeting on (alpha,n) data, November 2023

## Slide 2: Motivation
Stopping power affects TTY calculation
Also is important for IBA, dosimetry etc.
There are some discrepancies in the data
The goal: new data of stopping power for alpha-particles in carbon
Data from H.Paul database*
*Claudia Montanari, P. Dimitriou. The IAEA stopping power database, following the trends in stiopping power of ions in matter // Nuclear Instruments and methods in physics research Section B. 408. 2017 p.50-55

## Slide 3: Single scattering model
k – kinematic factor
E0
ER
kER
EA
Detector
Carbon target
∠α
∠β
x
Resonant scattering usually occurs on light nuclei
Method requires:
Thick target
Suitable resonances
Chart: Excitation function
ER
Chart: Backscattering spectrum
EA
Resonances in the excitation function lead to anomalies of similar shape in the spectrum.

## Slide 4: Method
Fitting a shape of stopping power
Normalization via RBS analysis
Excitation function
Backscattering spectrum

## Slide 5: Experimental setup
Target (pyrolytic graphite)
Current integrator
PIPS detectors at 150° and 170°
Preamplifiers
Spectrometry amplifiers
Two channel ADC
Accelerator work station
1
3
3
2
4He++
6
7
4
5
4
5
Scattering chamber
-300V

## Slide 6: Acquired spectra
Excitation function
Spectra examples
Resonance energy
Anomaly energy
The energy of anomaly was found as local extremum using 3-degree polynomial fitting

## Slide 7: Straggling correction
Chart: Eα (кэВ)
| 4350 | 4370 | 4390 | 4410 | 4430 | 4450 | 4470 | 4490 | 4510 | 4530 | 4550 | 4570 | 4590 | 4610 | 4630
ZBL 170 | 2.3089 | 2.212 | 2.4199 | 2.8882 | 3.0596 | 3.3824 | 3.7042 | 3.9902 | 3.5699 | 3.742 | 4.3821 | 4.3329 | 4.4053 | 3.8869 | 2.8912
SRIM 170 | 2.0538 | 2.7997 | 2.9707 | 3.0736 | 3.2335 | 3.6055 | 3.8683 | 4.0876 | 4.3088 | 4.5731 | 4.1993 | 3.6387 | 3.9273 | 3.1958 | 2.2227
ZBL 150 | 3.2319 | 3.8915 | 4.1475 | 4.6901 | 5.4811 | 5.4694 | 6.329 | 6.1962 | 6.8539 | 6.7425 | 7.1471 | 6.4251 | 6.2183 | 5.4643 | 4.5445
SRIM 150 | 2.5432 | 3.3737 | 3.7246 | 4.2804 | 4.8379 | 5.0483 | 5.8309 | 5.9041 | 6.5348 | 6.5853 | 6.7523 | 6.5029 | 6.7006 | 6.1292 | 5.6496
Energetic straggling affects anomaly position in spectra
Comparing of anomaly position with taking into account straggling and excluding
The energy shift mainly depends on angle
Energy shift due to straggling

## Slide 8: Stopping power normalization
Optimization was carried out by simulated annealing  energy dependency
Chart: Energy (channel)
Fitting procedure
Additional spectrum for 1990 keV
Normalization was carried out using standard SIMNRA utilities  absolute value

## Slide 9: Results
Uncertainty | Relative value
Anomaly energy | 0.7 %
Initial energy | <<1%
Optimization | 2-3 %
Normalization | 2-3 %
Total | ~3 %
Obtained stopping power
Stopping power function was approximated by:
P0 | 2.88 E2
P1 | -9.78 E1
P2 | 1.52 E1
P3 | -1.5 E0
P4 | 9.17 E-2
This work
ZBL
SRIM
ASTAR
KKK
H.Paul
Tosaki

## Slide 10
Chart: E, channels
Chart: E, channels
Validation
We tested stopping power using M. Mayer`s data *
SIMNRA-7 simulation reproduces spectra much better if our stoppings is taken into account **
These data were used in our 13C(α,n)16O experiment ***
**T.L. Bobrovskiy et al. Determination of stopping power for light ions using resonance backscattering // Nuclear Instruments and methods in physics research Section B. Volume 543, October 2023, 165094
***P.S. Prusachenko et al. Experimental study of thick target yield from the 13C(α,n)16O reaction // Nuclear science and engineering. DOI: 10.1080/00295639.2023.2236477
*M. Mayer, Statistical analysis of cross-section data for 12C(4 He,4 He)12C backscattering, Nucl. Instr. Meth. Phys. Res. B 285 (2012) 116–124.

## Slide 11: Future plans
Measuring the stopping power of actinide compounds
Checking Bragg-Kleeman rule
Target is prepared
Waiting for beam time

## Slide 12: Summary
New data on stopping power for α-particles in carbon were obtained
A new approach was used
The accuracy of the data was estimated to be approximately 3%.

## Slide 13
Thank you for attention!